## Slide 1
Peng Mei
Department of Electronic Systems
Email: mei@es.aau.dk
Bipolar Junction Transistors

## Slide 2
Learning objectives:
Physical structure of a NPN transistor
Three basic circuit types of a NPN transistor
Current components of a NPN transistor
I-V characteristic

## Slide 3
Notes: Energy of conservation.
The frequency of the signal is the same. (no frequency conversion)

## Slide 6
First BJT in 1948 at the Bell Telephone Lab
John Bardeen
William Schockley
Walter Brattain
Notes: Can you identify which is collect lead, which is emitter lead, and which is base lead

## Slide 8
First BJT in 1948 at the Bell Telephone Lab
John Bardeen
William Schockley
Walter Brattain
Collector
lead
Emitter
lead
Base lead

## Slide 9
Depletion
region
Depletion
region
Depletion
region

## Slide 10
Notes: Base región is quite narrow in NPN BJT, while it is quite wide in PN diode. Otherwise, the current cannot flow from collector to emitter.

## Slide 11
3 areas, each with its own contact:
N-doped area: “Emitter (E or e)”
P-doped area: “Base (B or b)”
N-doped area: “Collector (C or c)”
Emitter area: highly doped density
Collector area: low doped density and large area
Base area: thin, around 1 – 2 um, lowest doped density
NPN
PNP
E
B
C

## Slide 12
Notes: Base región is quite narrow in NPN BJT, while it is quite wide in PN diode. Otherwise, the current cannot flow from collector to emitter.

## Slide 13
Common emitter
Common base
Common collector
Quite similar

## Slide 14
Emitter: Emits electrons;
Collector: Collects electrons;
Current components:
Electrons E B C => Collector current (iC) (BE voltage controls the current)
Electrons E B => Base current (iB)
Holes B E => Base current (iB)
How about emitter current (iE)?
What is forward biased
and reverse biased?
Notes: KCL(Kirchhoff’s current law): the current flowing into a node (or a junction) must be equal to the current flowing out of it.
Ie = Ib + Ic

## Slide 15
Mode | EBJ | CBJ
Cutoff | Reverse | Reverse
Active | Forward | Reverse
Saturation | Forward | Forward
Notes: When different voltages are applied to the EB and CB, the NPN transistor Will work at different modes.

## Slide 16
AE: cross-sectional area of emitter area
q : electron charge = 1.6 * 10 -19 C
Dn: diffusivity of electrons
ni : number of thermally generated electrons
NB: doping density in base
WB: the width of base
T : absolute temperature
Could be controlled by manufacturing.
Temperature dependent
iC ~ υBE curve:
At active mode

## Slide 17
How much does iC change if vBE increases by 60mv?
A

## Slide 18
Uon
Si: 0.5 – 0.7 V
Ge: 0.1 – 0.3 V
Active mode:
Emitter forward biased;
Collector reverse biased;
υCE > υBE
Similar to a
PN junction
iB ~ υBE curve:
Notes: Si: silicon
Ge: Germanium
Why the curve is shifting towards right when vce increase?

## Slide 19
The analytical relationship between υBE and iB
Electrons E B => Base current (iB)
Holes B E => Base current (iB)
(forget details)
(forget details)
Holes from
B to E
Electrons from
E to B
Big β, if:
W is small
NA << ND
Typically: 10 < β < 1000
Notes: Ic curve should be plot here.
Why ic is controlled by VBE rather tan VCE?

## Slide 20
Temperature effects on I-V curves

## Slide 21
Thanks